## Slide 1
1.0 10E6 10E12 10E18 10E24
HZ
Long radio waves
AM
Short
Waves
FM,TV
Microwaves
Infrared
Visible light
Ultraviolet
light
X-rays
Gamma rays
The electromagnetic spectrum
A LITTLE HISTORY ON WIRELESS NETWORKS.
PRIOR TO THE NINETEENTH CENTURY, SCIENTISTS THOUGHT
VISIBLE LIGHT WAS THE ONLY WAVELENGTH OF THE
ELECTROMAGNETIC SPECTRUM.

## Slide 2
Wireless connectivity provides a new layer of flexibility
and services to environments and users that can not
be well served by traditional coaxial or fiber connections.
Advantages Disadvantages
Ease of installation Environmental limits
Ease of modification Range
Mobility Throughput (is on the
Portability increase)
Interconnectable Unreliable today
Expandable
Easily segmented
Broad range of coverage
and options

## Slide 3
Network technologies and radio communications were
brought together for the first time in 1971 at the University
of Hawaii.
The ALOHANET as it was called was a reliable BI-directional
communications network, in a star topology, between the
central computer and each of the remote stations.
In 1985, the FCC made commercial development of radio-
based LAN components possible by authorizing the public
use of the Industrial, Scientific and Medical (ISM) E-M band.
This band resides between 902 MHZ and 5.85 GHZ, which
is just above the cellular phone frequencies.

## Slide 4
In 1990, NCR & Motorola began shipping WaveLan and Altair
wireless adapters respectively.
Several months later companies such as Proxim, Xircom,
Windata and others joined in and the need for a standard
became evident.
The Institute for Electrical and Electronic Engineers (IEEE)
802 working group, responsible for development of LAN
standards such as Ethernet (802.3) & Token Ring (802.5)
initiated the 802.11 protocol.
The standard should be completed in 1997, but most
manufacturers today are building equipment based upon
the 802.11 protocol.

## Slide 5
Today, there are three regions of E-M spectrum that are
utilized for network communications.
1) Infrared signals
The wavelength is in the range of 900 nanometers in an
Infrared system.
There has to also exist a direct line of sight between the
transmitter and the receiver, although angles of +/- 30
degrees can be tolerated; furthermore, signals can
also be bounced on smooth surfaces.
Infrared signals can operate at relatively high speeds.
Current products operate at 16 Mb/s, but the limits as they
are calculated by today’s transmitter / receiver technology
is around 100 Mb/s.

## Slide 6
Radio signals in more detail
There are three regions of the E-M spectrum utilized by these
waves: 902-928 Mhz, 2.4-2.484 Ghz and 5.725-5.850 Ghz.
There are two popular methods of transmitting / receiving
data over a frequency spectrum. These methods were used
by the military in the 1970’s for secure transmission.
FHSS- Frequency hopping spread spectrum involves dividing
a range of radio spectrum into individual channels. The
Transmitter and the reviver follow a predetermined pattern
to hop from one channel to the next to send and receive data.
DSSS- Direct sequence spread spectrum transmissions
occur over a continuos band of frequencies. A unique code
is applied to the input signal, and the receiver uses the same
code to recover the information.

## Slide 7
One of the goals for wireless connectivity is to make it
transparent at the application / user level.
Lets look at the open systems Interconnect (OSI) model.
application
presentation
session
transport
network
data link
physical
logical link control
LLC 802.2
Medium Access Control
802.3,802.4,802.5,802.11
Physical layer
Data Link
Physical
layer

## Slide 8
The foundation protocol is at the medium Access Control
(MAC) level of the Data Link Layer.
Remember, this specifies which nodes will have access to the
medium of transmission.
The MAC-part of the 802.11 standard is named Distributed
Foundation Wireless Medium Access Protocol (DFWMAC),
and is based on a CSMA/CA type access protocol with a
rotating back-off window.
In order to understand this scheme lets review Ethernet’s
CSMA/CD operation.
Nodes will listen to the medium (wired) for a free slot to
transmit their packets. When two or more nodes begin to
transmit simultaneously, a collision occurs and the packets
are backlogged. The packets are then re-transmitted with the
probability of q=1/2^i; i=no. of collisions for that packet

## Slide 9
CSMA/CA Mechanism
Station Senses the medium, if busy then waits until
transmission done plus an additional time (DIFS).
It will then calculates randomly a slot within a contention
window to start transmitting, and finally it starts a
countdown to that time slot.
During the countdown if another station begins transmitting
it will freeze its counter until that transmission is done.
Collisions can now occur if and only if two stations pick the
same slot within the Contention Window to transmit; if that
occurs both stations will recalculate a future slot within a
doubly larger Contention Window.

## Slide 10
Backoff Time=INT(CW*Random())*slot time
CW=Integer between CWmin and CWmax
Random()=Random number between 0-1.
Slot time= Constant value of time
FRAME
CW
Station A
Station B
Station C
Station D
Backoff
FRAME
CW
FRAME
FRAME
CW
Example of DFWMAC Scheme

## Slide 11
Backbone
Access point
Access point
Roaming will enable a station to seemlessly move from one
are of operation to the next.

## Slide 12
Application
Presentation
Session
TCP
IP
802.11
DSSS
Application
Presentation
Session
TCP
IP
IP
802.11
DSSS
Data link
Physical
Data link
Physical
Access point (Bridge)
Wireless model
Wired model
Wireless to Wired model